## Slide 1
Hybrid Adaptive Clock Management for FPGA Processor Acceleration
Alexandru Gheolbanoiu1, Lucian Petrica1, Sorin Cotofana2 1University POLITEHNICA of Bucharest
2Technical University of Delft

## Slide 2: Outline
Background
Motivation
Instruction-Level Frequency Scaling
Clock Stretching in FPGA
Hybrid Adaptive Clock Management
Evaluation
Conclusion

## Slide 3: Background
Soft Processors
Parallel Processors
OPINCAA Soft Vector Processor

## Slide 4: Background
OPINCAA designed for
  scalability (10s – 100s of PEs)
  portability (FPGA-agnostic)
Virtex 6 (ML605)
350 PEs
Zynq (Zedboard)
200 PEs

## Slide 5: Motivation
Not all instructions are created equal on FPGA
Performance degrades differently under congestion and resource constrains

## Slide 6: Motivation
Multiplication vulnerable and
Tools Optimize for Path Balancing
Net Result - Long routes or deep paths in single instruction result in entire processor slow-down

## Slide 7: Instruction-Level Frequency Scaling
VASILE: Vector Architecture for frequency Scaling at the Instruction LEvel
  Instructions have individual Fmax targets
  Clock multiplexing (Xilinx BUFGCTRL)

## Slide 8: Instruction-Level Frequency Scaling
VASILE: Vector architecture for Frequency Scaling at the Instruction Level
  Instructions have individual Fmax targets
    Baseline 125 MHz
    Multiplication tops at 117 MHz
    All other instructions capable of 167 MHz
  Clock multiplexing (Xilinx BUFGCTRL)
    Large multiplexing penalty (up to 3x period)
    Work-around by loop tiling

## Slide 9: Instruction-Level Frequency Scaling

## Slide 10: Instruction-Level Frequency Scaling

## Slide 11: Instruction-Level Frequency Scaling

## Slide 12: Instruction-Level Frequency Scaling

## Slide 13: Instruction-Level Frequency Scaling

## Slide 14: Instruction-Level Frequency Scaling
No tiling:
6 clock
switches
With tiling:
2 clock
switches
Tiling limited by number of registers and data dependency !

## Slide 15: Clock Stretching for FPGAs
Idea: Stretch clock instead of Multiplexing
  BUFGCTRL predictable when clocks have same F
  TSW equals phase offset (symmetric for 180)
  Continuous switch == continuous stretch

## Slide 16: Clock Stretching for FPGAs

## Slide 17: Clock Stretching for FPGAs
Advantages
  Instant T extension (no need for Tiling)
Disadvantages
  More resources
    MMCM + multiple BUFGCTRLs + LUTs/FFs
  Lower Fmax
    Uses fabric logic
  Stretch amount is not continuous

## Slide 18: Clock Stretching for FPGAs
TE is the difference between achievable and desired T
Target: recover TE

## Slide 19: Hybrid Adaptive Clock Management
Merge clock multiplexer with stretcher
Dynamic decision mux/stretch

## Slide 20: Hybrid Adaptive Clock Management
Merge clock multiplexer with stretcher
Dynamic decision mux/stretch
  Monitor instruction stream
  Estimate execution time for last N instructions
    By Muxing
    By Stretching
  Assume predictable instruction stream
    Deep buffer or
    Simple, data-intensive work

## Slide 21: Evaluation
Implemented HACM in VHDL, targeting Zynq 7020
Slow instruction is multiplication (8.5ns to 6.1ns)
Measures mux switch time in simulation
Performed post P&R simulations
  Clock switch time estimation
  SSD (~25% multiply)
  ANN (mostly dot product, multiply-reduce)
  FIR (~10% multiply)

## Slide 22: Evaluation
Characterize BUFGCTRL switch time (for use in HACM)

## Slide 23: Evaluation
Instruction buffer 100-deep
  Small buffer vulnerable to decision “ripple”
  Larger buffers slow to react
Untiled benchmarks
Algorithm | SSD | NN | FIR
Clock Multiplexing [ms] | 1.28 | 3.65 | 12.75
Hybrid [ms] | 1.13 | 3.13 | 12.07
Speedup | 1.11 | 1.14 | 1.05

## Slide 24: Evaluation
Tiled SSD Evaluation

## Slide 25: Evaluation
Decision block of HACM requires 3 multipliers
CS/HACM slow compared to CM
Power dissipation accuracy uncertain
ACM Type | CM | CS | Hybrid
LUT | 0 | 5 | 52
FF | 0 | 3 | 33
DSP48 | 0 | 0 | 3
BUFGCTRL | 1 | 4 | 6
FMAX | 500+ | 350 | 350
Power [mW] | 0 | 100 | 100

## Slide 26: Conclusion
Instructions suffer congestion differently in FPGAs
Overall impact reduced through instruction-level frequency scaling
Clock multiplexing is simple but has long switch time
Clock stretching is an alternative, cannot provide accurate frequency synthesis
Hybrid clock management best of both worlds

## Slide 27: Open Questions
Applying concepts to other soft processors
Does it work on other FPGA architectures (Altera)
Power dissipation
Larger, more varied benchmarks
Better synthesis tool support

## Slide 28
Thank You
Q&A