## Slide 1: VASILE: A Reconfigurable Vector Architecture for Instruction Level Frequency Scaling
Lucian Petrica | Valeriu Codreanu | Sorin Cotofana
University Politehnica of Bucharest | University of Groningen | Delft University of Technology
lucian.petrica@arh.pub.ro | v.b.codreanu@rug.nl | s.d.cotofana@tudelft.nl

## Slide 2: Outline
FPGA Vector Processors
  Introduction
  Problem statement
VASILE Architecture
  Hardware Architecture
  Design Methodology
  Software Support
Performance Evaluation

## Slide 3: FPGA Vector Processors: Introduction
Conveniently add custom vector capability to general-purpose processor, on-demand
Application areas: cryptography, computer vision, speech processing etc
Notes: There have been several projects to develop FPGA vector coprocessors, including VENICE, VESPA, Delft’s MOLEN and our own work on the ConnexArray for computer vision (perhaps mention the HEART paper and results)
Explain the components: PEs in particular have register files, local memory, ALUs etc

## Slide 4: FPGA Vector Processors: The Problem Statement
FPGA architectures are non-uniform
Logic, Memory and DSP placed in columns
Column placement is device-specific
Memory and DSP are distant
Notes: The non-uniform column architecture of FPGAs is dictated by manufacturing considerations and is not likely to change in the future; it affects both Xilinx and Altera
The picture is of the Zynq7020, extracted from Xilinx PlanAhead floorplanning software
In this particular case, the maximum distance between DSP columns is half the length of the die, and the maximum distance between memory columns is 30% of die length

## Slide 5: FPGA Vector Processors: The Problem Statement
FPGA non-uniformity affects design timing
  Under high logic utilization, timing becomes significantly worse as logic must be placed far from DSP or memory resources
Portability is reduced
  Timing is device-specific and must be solved per-device
Typical solution: design for worst-case timing scenario, increasing area and power
Notes: On the Zynq7020 design, depending on logic placement, wires to and from the DSP an memory columns can be 25% and 15% of die length respectively, with correspondingly high propagation times
This affects instructions differently: multiplication and memory-related instructions most likely to be affected
The typical solution is to over-specify the architecture with regard to timing (add pipelines, take larger timing margins). This approach leads to increased design area and power consumption. Alternatively, the designer can choose to accept the performance loss.

## Slide 6: VASILE: Vector Architecture for Scaling at Instruction LEvel
Implement pseudo-asynchronous operation
  Limit timing impact to a subset of instructions
  Run clock at the frequency required by the executing instruction
Optimize instructions based on their relative frequency
  “make the common case fast”

## Slide 7: VASILE
Re-evaluate PE architecture
  Divide instructions into classes based on FPGA resources used:
Instruction Class | FPGA Resource
Algebra | Logic (LUTs)
Multiplication | Embedded Multipliers (DSP)
Memory | Embedded RAM
Communication | Routing

## Slide 8: VASILE
Re-evaluate PE architecture
  Divide instructions into classes based on FPGA resources used
  Group logic of each instruction class into an Instruction Unit
Notes: The register file, flags, operand registers and write-back multiplexer are optimized for the highest frequency of the system (the fastest IU)

## Slide 9: VASILE
Re-evaluate PE architecture
  Divide instructions into classes based on FPGA resources used
  Group logic of each instruction class into an Instruction Unit
  Add a clock switching unit
    Switching penalty incurred
Notes: The clock switching unit can be commanded by hardware or software inspection of the instruction stream; it must ensure that the clock has switched when the corresponding instruction enters the IU

## Slide 10: VASILE
Re-evaluate PE architecture
Re-evaluate hardware design methodology
  Separate timing constraints for each IU
  Tighten or loosen IU constraints by inspecting application profiling data (relative instruction densities)
Notes: Explain that instruction density for a given instruction class is the ratio of instruction occurrences from that class and total number of instructions

## Slide 11: VASILE
Re-evaluate PE architecture
Re-evaluate hardware design methodology
Introduce architecture-specific compilation
  Minimize clock switching by tiling and clustering instructions from the same class together
Use dynamic reconfiguration
  VASILE instances can be time-multiplexed in the FPGA to ensure the best performance
Notes: As presented in the design methodology, the IUs are optimized based on profiling data from a target application; Therefore, other applications may perform badly; To solve this, several VASILE instances may be generated for different applications and loaded into the FPGA on-demand at run-time

## Slide 12: Evaluation
Target Zynq7020 device
Used SAD, SSD and Gaussian convolution
Instruction Class | Baseline Frequency [MHz] | Maximum Frequency [MHz] | Average Density [%]
Algebra | 125 | 163 | 53
Multiplication | 125 | 117 | 33
Memory | 125 | 160 | 11
Communication | 125 | 160 | 3
Notes: Baseline frequency is computed by setting all IU constraints to the same value, and running an FPGA build to verify the highest attainable speed (therefore it is the highest attainable system frequency without IU differentiation)

## Slide 13: Evaluation
Target Zynq7020 device
Used SAD, SSD and Gaussian convolution
Used BUFGMUX primitive for clock switching
Manually applied tiling and clustering
Algorithm | Tile Size | Clock Switches per Outer Loop | Speedup
SAD | - | 0 | 1.28
SSD | 30 | 2 | 1.10
Convolution | 10 | 4 | 0.90
Notes: The BUFGMUX switches between two clock sources in a time which is at most 3 clock periods of the slower clock
Because of the clock switch time and maximum frequencies, we selected only two classes: multiplication and non-multiplication instructions
SAD does not need tiling because it has no multiplications
Speedup is calculated versus the baseline frequency implementation
The large number of clock switches for convolution means we have slow-down instead of speed-up

## Slide 14: Evaluation
Energy consumption evaluations carried out on realistic SIFT image matching workload (1 feature extraction and database match per second)
Power gating assumed off-chip for FPGA fabric, clock gating on-chip for the Zynq
The system is kept in low-power modes whenever it is not computing
Both static and reconfigurable implementations tested
Notes: SIFT image matching utilizes two of the kernels previously discussed: SAD and convolution
We considered scale-space construction on 1280x720 pixel image
We considered an average of 1000 keypoints to result from each SIFT pass, and matched those against 10 thousand keypoints in a database
The match happens once every second, after it ends the system goes into low-power mode

## Slide 15: Evaluation
Implementation | Baseline | CS | RCS
T convolution [ms] | 180 | 198 | 180
T matching [ms] | 560 | 437 | 437
T total [ms] | 740 | 635 | 617
FPGA Power [mW] | 600 | 636 | 636
Zynq Total Power [mW] | 1620 | 1656 | 1656
Energy Consumption [mJ] | 1199 | 1053 | 1021
Speedup | 1 | 1.16 | 1.20
Relative Energy | 1 | 0.88 | 0.85
Notes: The reconfigurable implementation does a little better by switching between the baseline and slow-multiply instances of the vector processor; the baseline instance does the convolution, and the slow-multiply does SAD
Energy consumption is for one second of run-time (therefore equivalent to average power consumption)

## Slide 16: Conclusion
VASILE decouples timing of instructions in order to avoid timing penalties from FPGA non-uniform resource placement
On the tested algorithms, speed-up of up to 28% and energy reduction of up to 15%
Future work: VASILE compiler, automation of design methodology

## Slide 17: Thank You Q & A